## Slide 1
CHAPTER 12
Quality Management
Key Takeaways & the Role of AI
From TQM to Six Sigma to Generative & Agentic AI
Dr. Benyawarath “Yaa” Nithithanatchinnapat
OSCM
BCOR 440/IE 425 Spring 2026

## Slide 2
Today's Roadmap
01
What is Quality?
Dimensions, design vs. conformance
02
Total Quality Management
TQM philosophy & the cost of quality
03
Six Sigma & DMAIC
The 5-phase methodology + Lean Six Sigma
04
The 7 Basic Quality Tools
Fishbone, Pareto, control charts & more
05
Quality Certifications
ISO 9000, ISO 14000, and supply chain quality
06
AI in Quality Management
Predictive, Generative & Agentic AI applications

## Slide 3
What is Quality?
Design Quality
Inherent value of the product in the marketplace
7 Dimensions (Exhibit 12.2):
Performance
Features
Reliability / Durability
Serviceability
Aesthetics
Perceived Quality
Conformance Quality
How well the product meets design specs
Determinants of Quality:
Quality at the source — the person who does the work is responsible
Process design ensures specs are met during production
"Don't inspect quality in — build it in"
KEY INSIGHT: Quality is a strategic decision (design) AND an operational discipline (conformance)

## Slide 4
Cost of Quality (COQ)
Prevention Costs
Sum of all costs to prevent defects before they happen
e.g., Training, FMEA, quality planning, SPC systems
Appraisal Costs
Costs of inspection and testing to verify acceptability
e.g., Incoming inspection, testing equipment, audits
Internal Failure
Costs for defects caught within the system
e.g., Scrap, rework, re-testing, downtime
External Failure
Costs for defects that reach the customer
e.g., Warranty, recalls, lawsuits, brand damage
THE 1-10-100 RULE: $1 in prevention saves $10 in appraisal and $100 in failure costs

## Slide 5
Total Quality Management (TQM)
Managing the entire organization so that it excels on all dimensions of products and services important to the customer
GOAL 1
Careful design of the product or service
GOAL 2
Ensuring systems can consistently produce the design
Quality Thought Leaders
Crosby
Zero defects, conformance to requirements, quality is free
Deming
14 Points, reduce variation, system of profound knowledge
Juran
Quality trilogy: planning, control, improvement; vital few vs trivial many

## Slide 6
Six Sigma Quality
A philosophy and set of methods to eliminate defects by reducing variation in processes
3.4
DPMO at Six Sigma
99.99966% yield
DPMO = (Number of defects / (Opportunities per unit x Number of units)) x 1,000,000
Sigma Level | DPMO | Yield | Real-World Analogy
2σ | 308,537 | 69.1% | Losing luggage 1 in 3 flights
3σ | 66,807 | 93.3% | 1 hour unsafe drinking water/month
4σ | 6,210 | 99.38% | 1 lost article of mail per hour
6σ | 3.4 | 99.99966% | 1 defect per 294 years of production

## Slide 7
The DMAIC Cycle
The structured 5-phase problem-solving methodology of Six Sigma (developed at GE)
D
DEFINE
Identify customers and their priorities. Define the problem, scope, and goals.
M
MEASURE
Determine how to measure the process. Establish baseline performance.
A
ANALYZE
Determine the most likely causes of defects. Use data to find root causes.
I
IMPROVE
Identify means to remove the causes of defects. Test and implement solutions.
C
CONTROL
Determine how to maintain improvements. Monitor with control charts.

## Slide 8
The 7 Basic Quality Tools
Flowchart
Visual map of process steps and decision points
Define/Map the process
Check Sheet
Structured form to collect and tally data systematically
Measure phase
Pareto Chart
Bar chart ranking problems by frequency — the vital few
Analyze (80/20 Rule)
Fishbone Diagram
Cause-and-effect (Ishikawa) — 6M categories
Analyze root causes
Histogram
Frequency distribution of data — see the shape
Measure/Analyze
Scatter Diagram
Plot pairs of data to find correlations
Analyze relationships
Control Chart
Monitor process variation over time (UCL, LCL, CL)
Control phase

## Slide 9
Additional Tools & Quality Certifications
Advanced Six Sigma Tools
FMEA
Failure Mode & Effects Analysis — proactively identify & prioritize failure risks at each process stage
DOE
Design of Experiments — determine cause-and-effect relationships between process variables and output
Lean Six Sigma
Combines Six Sigma's defect-elimination with Lean's waste-reduction and JIT inventory
Poka-Yoke
Mistake-proofing mechanisms that prevent errors from occurring or catch them immediately
Quality Certifications
ISO 9000
International quality management standard. ISO 9001 specifies requirements for a QMS — documents processes, procedures, and responsibilities for achieving quality objectives.
ISO 14000
Environmental management standard. Ensures organizations minimize harmful environmental effects and continually improve environmental performance.

## Slide 10
NOW LET'S TALK ABOUT
AI in Quality Management
How Predictive, Generative, and Agentic AI are transforming every concept we just covered

## Slide 11
Three AI Paradigms in Quality
Predictive AI
Uses historical data to forecast outcomes and detect patterns before they become problems
Examples:
Predicting equipment failures, forecasting defect rates, demand-driven quality planning
Strongest in MEASURE & ANALYZE
Generative AI
Creates new content, designs, and solutions — augments human analysis and documentation
Examples:
Auto-generating FMEA documents, writing SOPs, creating training materials, analyzing root causes from text data
Strongest in DEFINE & IMPROVE
Agentic AI
Autonomous AI systems that perceive, decide, and act — closing the loop without human intervention
Examples:
Self-adjusting process parameters, autonomous inspection robots, AI orchestrating entire DMAIC projects
Strongest in CONTROL & across all phases

## Slide 12
AI Transforms the Cost of Quality
Prevention
Predictive AI forecasts which raw materials or conditions will lead to defects before production starts. GenAI auto-generates FMEA documents and risk assessments.
Tesla uses ML to predict battery cell failure modes during design phase
Appraisal
Computer vision (Predictive AI) performs 100% automated inspection at line speed — far beyond human sampling rates. Eliminates manual inspection bottleneck.
BMW uses AI vision systems inspecting 300 welds per car body in seconds
Internal Failure
Agentic AI detects out-of-spec conditions and self-adjusts process parameters in real-time — catching defects before they become scrap.
Siemens Amberg factory: AI reduces defect rate to 12 per million
External Failure
Predictive AI monitors field data from IoT sensors to predict warranty claims before they happen. GenAI writes customer communication.
John Deere uses predictive maintenance AI to prevent field equipment failures
AI SHIFTS THE COST CURVE: Investment moves from appraisal/failure to AI-powered prevention systems

## Slide 13
AI Supercharges Every DMAIC Phase
Phase | Predictive AI | Generative AI | Agentic AI
DEFINE | NLP analyzes thousands of customer reviews to extract VOC patterns | GenAI drafts project charters, problem statements, SIPOC diagrams | AI agents auto-triage incoming complaints by severity
MEASURE | Automated Gage R&R, ML-based measurement system validation | GenAI creates data collection plans and sampling strategy docs | IoT sensor agents autonomously collect and validate data streams
ANALYZE | ML models find hidden correlations humans miss in complex data | GenAI generates hypothesis lists, interprets statistical outputs in plain English | AI agents run automated hypothesis testing across variables
IMPROVE | Simulation models predict outcomes of proposed changes | GenAI designs experiments (DOE), generates implementation plans | Self-optimizing systems implement and test improvements autonomously
CONTROL | Predictive monitoring anticipates drift before out-of-control | GenAI writes SOPs, training materials, control plans | Agentic AI auto-adjusts parameters + triggers alerts without humans

## Slide 14
Agentic AI: The Future of Quality
Autonomous systems that perceive, reason, decide, and act in quality management
Self-Healing Production Lines
AI agents monitor sensors, detect anomalies, diagnose root causes, and adjust machine parameters — all without stopping production or calling an engineer.
Autonomous Quality Inspection
Vision AI agents make pass/fail decisions, route defects to appropriate rework stations, and update control charts in real-time — replacing traditional sampling.
AI-Orchestrated DMAIC
An AI agent manages an entire Six Sigma project: scoping the problem, collecting data, running analyses, recommending solutions, and monitoring results.
Supply Chain Quality Agents
AI monitors supplier quality metrics, predicts incoming material issues, automatically adjusts inspection levels, and renegotiates specs with vendor systems.

## Slide 15
Chapter 12 Key Takeaways
1
Quality has two dimensions: design quality (strategic, marketplace value) and conformance quality (operational, meeting specs)
2
TQM requires the entire organization — quality is everyone's job, not just a department
3
Cost of Quality reveals where money is actually being spent: prevention, appraisal, internal and external failure
4
Six Sigma (DMAIC) provides a structured, data-driven methodology for eliminating defects and reducing variation
5
The 7 basic quality tools + FMEA, DOE give you a practical analytical toolkit for every phase
6
AI is reshaping quality: Predictive AI detects patterns, Generative AI augments analysis, Agentic AI closes the loop autonomously

## Slide 16
Discussion
If an AI agent can autonomously run a DMAIC project, what is the quality engineer's new role?
Should companies trust Agentic AI to make real-time quality decisions with no human in the loop?
How does AI change the 1-10-100 Rule? Does prevention become essentially free?