## Slide 1
CHAPTER 13
Statistical Quality Control
Key Takeaways & the Role of AI
From Control Charts to Process Capability to AI-Powered Quality
Dr. Benyawarath “Yaa” Nithithanatchinnapat
OSCM
Spring 2026

## Slide 2
Today's Roadmap
01
Variation
Common (random) vs. assignable (special) causes
02
Inspection
When to inspect, where to inspect, how much
03
SPC — Attribute Charts
p-Charts & c-Charts for go/no-go data
04
SPC — Variable Charts
X-bar & R charts for continuous measurement
05
Process Capability
Cp, Cpk — can we meet spec?
06
AI in Quality Control
Predictive, Generative & Agentic AI applications

## Slide 3
The Enemy of Quality: Variation
All processes have variation. The goal of SQC is to detect when variation has a non-random, identifiable cause.
Common (Random) Variation
Inherent in every process — always present
Caused by many small, unavoidable factors
Process is "in control" when only common variation exists
Can only be reduced by fundamentally changing the process
Analogy: The slight wobble in every golf swing
Assignable (Special) Variation
Caused by specific, identifiable factors
Tool wear, new material lot, untrained operator
Process is "out of control" — must investigate and fix
SPC is designed to detect this type of variation
Analogy: A golfer suddenly slicing every shot because their grip changed
SPC GOAL: Separate the signal (assignable) from the noise (common) using statistical control limits

## Slide 4
Inspection: Where, When, How Much?
WHERE to inspect?
At the source (supplier), during production, or at the end. Inspect at stages where defects are costliest to miss.
HOW MUCH to inspect?
Trade-off: cost of inspection vs. cost of passing defective items. 100% inspection vs. sampling depends on defect cost.
Attributes vs. Variables?
Attributes = good/bad (binary). Variables = continuous measurement (weight, length, time). Choice determines which chart to use.
The SPC Decision Flow
1. Is process IN CONTROL? (SPC charts) → 2. Is process CAPABLE? (Cpk) → 3. START PRODUCTION

## Slide 5
SPC Control Charts: The Big Picture
Chart Type | Data Type | Scale | Measures | Example
X-bar & R Chart | Variable | Continuous | Process mean & range | Weight of soda bottles (grams)
p-Chart | Attribute | Binary (yes/no) | Proportion defective | Patient satisfaction survey (yes/no)
c-Chart | Attribute | Count | Number of defects | Number of defects per plastic sheet
Anatomy of a Control Chart
UCL
CL
LCL
Out-of-Control Signals (Exhibit 13.5)
One point beyond UCL or LCL
Two points near upper or lower control
Run of five above or below center line
Trend in either direction (progressive)
Erratic behavior (high variability)
Sudden shift in level

## Slide 6
Attribute Charts: p-Chart
Used when quality is measured as a proportion defective (binary: good/bad, pass/fail)
p-Chart Formulas
Step 1: Calculate average fraction defective
p-bar = Total defective / (Number of samples x Sample size)
Step 2: Calculate standard deviation
sp = SQRT( p-bar(1 - p-bar) / n )
Step 3: Calculate control limits
UCL = p-bar + z x sp (typically z = 3)
LCL = p-bar - z x sp (or 0 if negative)
Key Points
Binary data: pass/fail
Requires larger sample sizes than variable charts
Rule of thumb: at least 1 defective per sample
If LCL < 0, set LCL = 0
c-Chart: counts defects per unit (not proportion) — useful when total opportunities is unknown

## Slide 7
Variable Charts: X-bar & R Charts
When σ is KNOWN
X-bar Chart:
UCL = X-double-bar + zσx
LCL = X-double-bar - zσx
where σx = σ / √n
(σ = process SD, n = sample size)
Typically z = 3 (3-sigma limits)
When σ is UNKNOWN (New Process)
X-bar Chart:
UCL = X-double-bar + A₂ x R-bar
LCL = X-double-bar - A₂ x R-bar
R Chart:
UCL = D₄ x R-bar
LCL = D₃ x R-bar
A₂, D₃, D₄ from Exhibit 13.7(e.g., n=5: A₂=0.577, D₃=0, D₄=2.114)

## Slide 8
Process Capability: Cp & Cpk
In-control is not enough. The process must also be CAPABLE of meeting customer specifications.
Cp = (USL - LSL) / 6σ
Potential capability (if perfectly centered)
Cpk = min[ (USL - X̅) / 3σ , (X̅ - LSL) / 3σ ]
Actual capability (accounts for off-center mean)
If Cp > Cpk → the process mean has shifted off-center
Cpk | Rating | Meaning
< 1.0 | Not Capable | Process will produce defects beyond spec
1.0 - 1.33 | Barely Capable | Meets spec but with little margin
≥ 1.33 | Capable | Industry standard — recommended minimum
≥ 2.0 | Six Sigma | World-class, near-zero defects
REMEMBER THE SEQUENCE:
Step 1: Use control charts to verify process is IN CONTROL (stable, no assignable causes)
Step 2: Calculate Cpk to verify process is CAPABLE (can meet customer specs)
Step 3: Only then proceed to full production

## Slide 9
NOW LET'S TALK ABOUT
AI in Quality Control
How AI is revolutionizing inspection, SPC, and process capability analysis

## Slide 10
AI Transforms Inspection
TRADITIONAL
Human inspectors sample a fraction of output
Fatigue causes missed defects on later shifts
100% inspection is cost-prohibitive for most products
Trade-off: inspection cost vs. defect cost
Slow feedback loop — defects found hours later
AI-POWERED
Computer vision inspects 100% of units at line speed
Predictive AI: never gets tired, consistent 24/7
Detects micro-defects invisible to human eye
GenAI: auto-generates defect reports with root cause hypotheses
Agentic AI: auto-routes defects, adjusts parameters, updates charts
RESULT: The inspection cost vs. defect cost trade-off from Ch.13 is fundamentally changed — 100% inspection becomes affordable

## Slide 11
AI Supercharges SPC
Predictive AI
From Reactive to Predictive SPC
Traditional SPC detects out-of-control AFTER it happens. Predictive AI forecasts process drift 30-60 minutes before a control limit is breached, giving operators time to intervene.
Generative AI
Intelligent Chart Interpretation
GenAI reads control chart patterns and explains them in plain English: "Sample 15 shows a run of 5 above center — likely a material lot change. Recommend verifying incoming batch specs."
Agentic AI
Self-Correcting Processes
Agentic AI doesn't just detect the out-of-control signal — it autonomously adjusts machine parameters, logs the corrective action, updates the control chart, and notifies the team.
Predictive AI
Multivariate SPC
Classical SPC monitors one variable at a time. AI models monitor hundreds of sensor variables simultaneously, detecting complex patterns that no single X-bar chart could catch.

## Slide 12
AI Elevates Process Capability
Real-time
Cpk monitoring
Predictive: Dynamic Cpk
Instead of a static snapshot, AI calculates real-time Cpk that updates continuously as sensor data streams in. Predicts when Cpk will drop below 1.33 and alerts before it happens.
Seconds
vs. hours manually
GenAI: Capability Reports
Feed raw process data to GenAI and receive a complete capability study: histograms, normality tests, Cp/Cpk calculations, and plain-English recommendations — in seconds.
24/7
autonomous control
Agentic: Auto-Centering
When Cpk shows the process has drifted off-center (Cp > Cpk), agentic AI autonomously adjusts the process mean back to target — maintaining Six Sigma capability 24/7.

## Slide 13
Agentic AI: Closing the Quality Loop
Traditional SPC: detect → alert → wait for human → investigate → fix. Agentic AI does it all.
1
SENSE
IoT sensors feed real-time process data (temperature, pressure, dimensions)
2
DETECT
AI identifies out-of-control patterns or predicts drift before limits are breached
3
DIAGNOSE
GenAI analyzes root cause from historical patterns, material data, and maintenance logs
4
ACT
Agentic system autonomously adjusts parameters, re-routes production, or halts line
5
LEARN
Model retrains on new data, improving future predictions and reducing false alarms
CONTINUOUS LEARNING LOOP → Each cycle makes the system smarter

## Slide 14
Real-World AI + Quality Control
Tesla
Computer vision inspects every battery cell weld at Gigafactory — replaces sampling-based inspection with 100% AI inspection at production speed
Predictive AI
Amazon
Predictive models monitor warehouse packaging quality across 200+ fulfillment centers. Predicts defect spikes before they impact customers.
Predictive AI
Siemens
Amberg Electronics Plant uses agentic AI systems that autonomously control 75% of production — achieving 12 DPMO (near Six Sigma).
Agentic AI
Netflix
GenAI monitors streaming quality metrics (buffering, encoding defects) and auto-generates incident reports with root cause analysis.
Generative AI
AI doesn't replace SPC concepts — it makes them executable at machine speed and superhuman scale

## Slide 15
Chapter 13 Key Takeaways
1
All processes have variation — SPC separates common (random) from assignable (special) causes
2
Attribute data (p-chart, c-chart) vs. variable data (X-bar, R chart) — choose the right chart for the data type
3
Control limits are calculated from the process data (not spec limits!) — they tell you what the process IS doing
4
Process capability (Cpk) tells you if the process CAN meet specs — Cpk ≥ 1.33 is the industry standard
5
The sequence matters: In Control first → then Capable → then produce
6
AI transforms SPC: Predictive AI forecasts drift, GenAI interprets charts, Agentic AI closes the control loop autonomously

## Slide 16
Discussion
If AI can do 100% inspection, does sampling theory (acceptance sampling, p-charts) become obsolete?
Should we let agentic AI adjust process parameters without human approval? What are the risks?
A factory has Cpk = 0.67. Should they invest in AI-powered SPC or fix the process first? Why?